## Slide 1: Remote Sensing: physical basis and applications
Lecture 1: Physical basis and digital representation of remote sensing data
Thiago S. F. Silva
Graduate Program in Geography
Institute of Geosciences and Exact Sciences
São Paulo State University - UNESP
tsfsilva@rc.unesp.br

## Slide 2: Introductions
Thiago Sanna Freire Silva
tsfsilva@rc.unesp.br

## Slide 3: Course Overview
Day 1: The physical basis of remote sensing / Digital remote sensing images
Day 2: Spectroscopy of natural and artificial targets
Day 3: Image pre-processing
Day 4: Image processing: transformations
Day 5: Image Classification and Validation
Day 6: Where to get remote sensing imagery
Day 7: Automated remote sensing approaches
Days 8-9: Self-directed work on projects
Day 10: Project presentations

## Slide 4: What is remote sensing?
Remote sensing?
GIS?
Geomatics?
Spatial Analysis?
Geostatistics?

## Slide 5: What is remote sensing?
“The retrieval of quantitative information regarding the biophysical nature of objects in the Earth’s surface, by measuring the type and quantity of electromagnetic radiation reflected by these objects”
  Often, these measurements will be made in a way to form an image. But that is not a requirement for remote sensing.
  Remote sensing can also be done using other forms of energy, such as sound (acoustics).

## Slide 6: What is remote sensing?

## Slide 7
“Satellite Photos”

## Slide 8: The Physical Basis of Remote Sensing

## Slide 9: The physical basis of remote sensing
Remote sensing is a quantitative method
  What do we measure?

## Slide 10: The physical basis of remote sensing
Remote sensing is a quantitative method
  What do we measure? Electromagnetic radiation
  Where does it come from?

## Slide 11: The physical basis of remote sensing
Remote sensing is a quantitative method
  What do we measure? Electromagnetic radiation
  Where does it come from? Mostly, the Sun, but sometimes from the sensor itself
  Why use ER?

## Slide 12: The physical basis of remote sensing
Remote sensing is a quantitative method
  What do we measure? Electromagnetic radiation
  Where does it come from? Mostly, the Sun, but sometimes from the sensor itself
  Why use EMR?
    Fast (the speed of…light, 300,000 km/s)
    Can travel in a vacuum
    Well known physical properties

## Slide 13: Electromagnetic Radiation
Wave model
  Wavelength(λ) and frequency (ν)
Particle model
  Photon or quantum

## Slide 14: Electromagnetic spectrum
https://en.wikipedia.org/wiki/Electromagnetic_spectrum CC BY-SA 3.0

## Slide 15: Electromagnetic spectrum

## Slide 16: Electromagnetic Radiation
How do we produce EMR?

## Slide 17: Electromagnetic Radiation
How do we produce EMR?
  Any object with Tº > 0 K emits EMR
Planck’s Law
Wien’s Law
Stefan-Boltzmann’s Law

## Slide 18: Electromagnetic Radiation
What happens when EMR reaches a target?

## Slide 19: Electromagnetic Radiation
What happens when EMR reaches a target?

## Slide 20: Electromagnetic Radiation
What happens when EMR reaches a target?
reflectance
absorptance
transmittance

## Slide 21: Electromagnetic Radiation
What happens when EMR reaches a target?
reflectance
absorptance
transmittance

## Slide 22: Radiometry
  There are several ways to measure radiation
  Radiometric quantities build upon one another
https://russian-crafts.com/crafts-history/nesting-dolls-history.html

## Slide 23
Radiant Energy ()
Amount of energy in electromagnetic radiation
Unit: Joule (J)
Radiant Flux ()
Flow of EMR energy over time
Unit: Watt = J . s-1
Spectral Radiant Flux ()
Flow of EMR energy over time, at a given wavelength
Unit: W . nm-1

## Slide 24
Radiant Flux Density
Flow of EMR energy over time, per area
Unit: W . m-2
Can be referred to by two different names, depending on flow direction:
Surface
Surface
    Exitance ()
    Irradiance ()

## Slide 25
Radiance
Flow of EMR energy over time, per area, per solid angle
Unit: W . m-2 . sr-1
Angle Solid Angle

## Slide 26
Reflectance
Proportion of EMR that will be reflected by a target
Unit: unitless!
We can estimate reflectance from radiance and irradiance:

## Slide 27: O que nós realmente queremos?
  Reflectância (ρ, adimensional)
    Porcentagem da radiação incidente que é refletida
    Pode ser calculada a partir da relação entre irradiância e radiância:
    Por que queremos reflectância?

## Slide 28
Reflectance
Proportion of EMR that will be reflected by a target
Unit: unitless!
Reflectance is our “holy grail” in optical remote sensing. Why?
Let’s imagine a stable target, during summer and winter:
Summer:
Winter:

## Slide 29
Reflectance
Proportion of EMR that will be reflected by a target
Unit: unitless!
Reflectance is our “holy grail” in optical remote sensing. Why?
Reflectance in an intrinsic property of the target, independent from changes in illumination

## Slide 30: Reflectance
  Well…kind of independent.
  Lambertian targets will reflect equally in all directions (i.e. isotropic).
  Most targets are not Lambertian…but we assume they are.

## Slide 31: Reflectance
  Bidirectional Reflectance Distribution Function (BRDF)
  A mathematical function defining how much EMR is reflected in each direction

## Slide 32: THE NATURE OF DIGItaL REMOTE SENSING IMAGES

## Slide 33: Órbitas
Polar (Sol-síncrona): ~ 700km. Satélites de monitoramento terrestre

## Slide 34: Órbitas
Polar (Sol-síncrona): ~ 700km. Satélites de monitoramento terrestre

## Slide 35: Órbitas

## Slide 36: Órbitas

## Slide 37: Órbitas
Geoestacionária: ~ 36 mil km. Satélites meteorológicos e de comunicação

## Slide 38: Órbitas
Geoestacionária: ~ 36 mil km. Satélites meteorológicos e de comunicação
GOES-8

## Slide 39: Geometria de Aquisição
IFOV (Instantaneous Field of View): área observada por cada elemento detector
FOV/Swath: largura da faixa imageada

## Slide 40: Estrutura de uma imagem de SR
Pixels
Números digitais (níveis de cinza, valor de brilho, etc.)
Bandas

## Slide 41: Estrutura de uma imagem de SR
Bandas

## Slide 42: Resolução de uma imagem de SR
O que é uma imagem de “alta resolução”?

## Slide 43: Resolução de uma imagem de SR
O que é uma imagem de “alta resolução”?
As 4 resoluções do Sensoriamento Remoto
  Espacial
  Espectral
  Radiométrica
  Temporal

## Slide 44: Resolução Espacial
Qual a menor dimensão de um alvo que pode ser discriminada?
IFOV - Geralmente equiparada ao tamanho do pixel

## Slide 45: Resolução Espacial
Qual a menor dimensão de um alvo que pode ser discriminada?
IFOV - Geralmente equiparada ao tamanho do pixel

## Slide 46: Resolução Espacial
Qual a menor dimensão de um alvo que pode ser discriminada?
IFOV - Geralmente equiparada ao tamanho do pixel

## Slide 47
Resolução espacial:
Swath = 2330 km
Resolução Espacial = 500m
Sensor: MODIS

## Slide 48
Swath = 185km
Resolução Espacial = 30m
Arquivo – 305 MB
Sensor: Landsat TM
Resolução espacial:

## Slide 49
Swath = 2.6 km
Resolução Espacial = 0.5m
Arquivo – 141 MB
Sensor: Worldview-2
Resolução espacial:

## Slide 50: Resolução Espectral
Quantas bandas possui o sensor, e quão estreitas elas são?
  Pancromático, multiespectral, hiperespectral
  Nível de detalhe em que a assinatura espectral pode ser recuperada

## Slide 51: Resolução Espectral
Quantas bandas possui o sensor, e quão estreitas elas são?
  Pancromático, multiespectral, hiperespectral
  Nível de detalhe em que a assinatura espectral pode ser recuperada

## Slide 53: Resolução Radiométrica
Sensitividade do sistema de medição
  Qual o menor intervalo de radiância que consegue ser medido?
  Normalmente expresso como quantização :
    Sensores antigos: 8 bits = 28 = 256 possíveis valores
    Sensores mais novos: 12 ou 14 bits = 212 ou 214 = 4096 ou 16384 possíveis valores
8 bits = 256 níveis
4 bits = 16 níveis

## Slide 54: Resolução Temporal
Capacidade de repetição do imageamento
  De modo geral, inversamente relacionada à resolução espacial
  Pixels maiores = maior faixa imageadas = menor número de órbitas necessárias para retornar ao ponto de origem
Como melhorar:
  Órbitas geoestacionárias
  Side-looking
  Constelações
  SR aerotransportado

## Slide 55: O grande dilema do SR
Relação Sinal-Ruído (Signal to Noise Ratio, SNR)
  Quanto menor o sinal, pior a qualidade
http://www.photoreview.com.au/tips/shooting/how-to-control-image-noise

## Slide 56: Resolução e relação sinal-ruído (SNR)
Em geral, a determinação das resoluções é sempre um trade-off para se obter uma quantidade mínima de radiação adequada (SNR aceitável)
Tamanho do pixel x largura da banda x sensitividade do sensor x conteúdo de energia na banda de interesse
(x tempo de integração)

## Slide 57: Resolução e relação sinal-ruído (SNR)
Em geral, a determinação das resoluções é sempre um trade-off, até que se obtenha uma quantidade mínima de radiação adequada (SNR aceitável)
Tamanho do pixel x largura da banda x sensitividade do sensor x conteúdo de energia na banda de interesse
(x tempo de integração)
Ex:
Landsat TM banda 3: 30m | 630 – 690 nm (60nm) | 8 bits
MODIS banda 1: 250m | 620 – 670 nm (50 nm) | 12 bits
MODIS banda 13: 1km | 662 - 672nm (10nm) | 12 bits
Landsat OLI: 30 m | 640 – 670 (30nm) | 12 bits
Sentinel-3 OCLI banda 8: 300m | 660 – 670 (10nm) | 12 bits